## Slide 1
BEATTIE-NET // NETWORK ENGINEERING
Divide & Conquer: CompTIA 6-Step Troubleshooting
Mastering Systematic Fault Isolation & The Binary Search Diagnostic Method
01 // STOP GUESSING. START ISOLATING.
Amateur technicians guess and swap random parts. Enterprise network engineers and ethical hackers use formal deductive logic. Today you master the exact 6-step framework certified by CompTIA A+, Network+, and Security+.
02 // THE BINARY SEARCH METHOD
Linear troubleshooting through 7 OSI layers takes O(N) time. By testing at the OSI Midpoint (Layer 3/4), you eliminate 50% of the entire problem domain in a single CLI command: • ping 127.0.0.1 (NIC) • ping Gateway (LAN) • ping 8.8.8.8 (WAN) • nslookup (DNS)

## Slide 2
COMPTIA CORE CURRICULUM
The 6-Step Troubleshooting Lifecycle
Standard sequential methodology for CompTIA A+ / Network+ / Security+
STEP 1 // Identify the Problem
Question user, review system logs, identify changes, duplicate symptom.
STEP 2 // Establish Theory
Question the obvious. Formulate probable cause hypothesis (Top/Bottom/Divide).
STEP 3 // Test the Theory
Execute targeted test. If confirmed -> proceed; if disproven -> form new theory.
STEP 4 // Plan & Implement
Develop step-by-step action plan, anticipate side effects, execute solution.
STEP 5 // Verify & Prevent
Verify full system functionality with end user; apply preventative hardening.
STEP 6 // Document Everything
Record findings, actions, and outcomes in enterprise ticketing & KB.

## Slide 3
ENGINEERING WORKFLOW
The 5-Step Midpoint Diagnostic Ladder
Memorize these 5 sequential CLI commands to troubleshoot any network issue
[1] ping 127.0.0.1 — Local Loopback Adapter: Verifies local NIC driver and OS TCP/IP software stack.
[2] ping 192.168.1.1 — Default Gateway (LAN Exit): Verifies patch cable, wall jack, switch port, and router interface (L1-L3).
[3] ping 8.8.8.8 — External Public IP (WAN): Verifies ISP connection, NAT routing, and wide area internet path.
[4] nslookup google.com — DNS Name Resolution (L7): Verifies Port 53 DNS resolver, DNS caching server, and FQDN translation.
[5] Test-NetConnection -Port 443 — Application Port & Service: Verifies remote web service listening, TLS certificate, & stateful firewall.

## Slide 4
CTE REAL-WORLD LABS
Hands-On Troubleshooting Case Studies
Scenarios students will diagnose in today's companion lab activity
SCENARIO 1: The Silent Wall Jack [Physical Layer (L1/L2)] — Keystone jack miswire (pins 1-2 crossed). Wiremapping & punchdown repair.
SCENARIO 2: The 169.254 APIPA Storm [Network Layer (L3 DHCP)] — DHCP scope exhaustion. Subnet expansion and lease time optimization.
SCENARIO 3: The DNS Dilemma [Transport & DNS (L4/L7)] — 8.8.8.8 pings OK, domain name fails. Stale static DNS resolver fix.
SCENARIO 4: Rogue SSH Exfiltration [Incident Response] — Outbound Port 22 SSH tunnel alert. Endpoint quarantine and PID termination.
SCENARIO 5: The ARP Doppelgänger [Enterprise Security] — Man-in-the-Middle ARP poisoning. Dynamic ARP Inspection & DHCP Snooping.